## Slide 1: von Neumann architecture
Memory holds data, instructions.
Central processing unit (CPU) fetches instructions from memory.
Separate CPU and memory distinguishes programmable computer.
CPU registers help out: program counter (PC), instruction register (IR), general-purpose registers, etc.
© 2008 Wayne Wolf
Overheads for Computers as
Components 2nd ed.

## Slide 2
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
CPU + memory
memory
CPU
PC
address
data
IR
ADD r5,r1,r3
200
200
ADD r5,r1,r3

## Slide 3: Harvard architecture
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
CPU
PC
data memory
program memory
address
data
address
data

## Slide 4: von Neumann vs. Harvard
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Harvard can’t use self-modifying code.
Harvard allows two simultaneous memory fetches.
Most DSPs use Harvard architecture for streaming data:
  greater memory bandwidth;
  more predictable bandwidth.

## Slide 5: RISC vs. CISC
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Complex instruction set computer (CISC):
  many addressing modes;
  many operations.
Reduced instruction set computer (RISC):
  load/store;
  pipelinable instructions.

## Slide 6
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Instruction set characteristics
Fixed vs. variable length.
Addressing modes.
Number of operands.
Types of operands.

## Slide 7: RISC vs. CISC
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Complex instruction set computer (CISC):
  many addressing modes;
  many operations.
Reduced instruction set computer (RISC):
  load/store;
  pipelinable instructions.

## Slide 8
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Instruction set characteristics
Fixed vs. variable length.
Addressing modes.
Number of operands.
Types of operands.

## Slide 9: Programming model
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Programming model: registers visible to the programmer.
Some registers are not visible (IR).

## Slide 10: Multiple implementations
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Successful architectures have several implementations:
  varying clock speeds;
  different bus widths;
  different cache sizes;
  etc.

## Slide 11: CPUs
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Caches.
Memory management.

## Slide 12: Caches and CPUs
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
CPU
cache
controller
cache
main
memory
data
data
address
data
address

## Slide 13: Cache operation
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Many main memory locations are mapped onto one cache entry.
May have caches for:
  instructions;
  data;
  data + instructions (unified).
Memory access time is no longer deterministic.

## Slide 14: Terms
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Cache hit: required location is in cache.
Cache miss: required location is not in cache.
Working set: set of locations used by program in a time interval.

## Slide 15: Types of misses
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Compulsory (cold): location has never been accessed.
Capacity: working set is too large.
Conflict: multiple locations in working set map to same cache entry.

## Slide 16: Memory system performance
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
h = cache hit rate.
tcache = cache access time, tmain = main memory access time.
Average memory access time:
  tav = htcache + (1-h)tmain

## Slide 17: Multiple levels of cache
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
CPU
L1 cache
L2 cache

## Slide 18: Multi-level cache access time
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
h1 = cache hit rate.
h2 = rate for miss on L1, hit on L2.
Average memory access time:
  tav = h1tL1 + (h2-h1)tL2 + (1- h2-h1)tmain

## Slide 19: Replacement policies
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Replacement policy: strategy for choosing which cache entry to throw out to make room for a new memory location.
Two popular strategies:
  Random.
  Least-recently used (LRU).

## Slide 20: Cache organizations
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Fully-associative: any memory location can be stored anywhere in the cache (almost never implemented).
Direct-mapped: each memory location maps onto exactly one cache entry.
N-way set-associative: each memory location can go into one of n sets.

## Slide 21: Cache performance benefits
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Keep frequently-accessed locations in fast cache.
Cache retrieves more than one word at a time.
  Sequential accesses are faster after first access.

## Slide 22: Direct-mapped cache
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
valid
=
tag
index
offset
hit
value
tag
data
1
0xabcd
byte byte byte ...
byte
cache block

## Slide 23: Write operations
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Write-through: immediately copy write to main memory.
Write-back: write to main memory only when location is removed from cache.

## Slide 24: Direct-mapped cache locations
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Many locations map onto the same cache block.
Conflict misses are easy to generate:
  Array a[] uses locations 0, 1, 2, …
  Array b[] uses locations 1024, 1025, 1026, …
  Operation a[i] + b[i] generates conflict misses.

## Slide 25: Set-associative cache
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
A set of direct-mapped caches:
Set 1
Set 2
Set n
...
hit
data

## Slide 26: Example: direct-mapped vs. set-associative
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf

## Slide 27: Direct-mapped cache behavior
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
After 001 access:
  block tag data
  00 - -
  01 0 1111
  10 - -
  11 - -
After 010 access:
  block tag data
  00 - -
  01 0 1111
  10 0 0000
  11 - -

## Slide 28: Direct-mapped cache behavior, cont’d.
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
After 011 access:
  block tag data
  00 - -
  01 0 1111
  10 0 0000
  11 0 0110
After 100 access:
  block tag data
  00 1 1000
  01 0 1111
  10 0 0000
  11 0 0110

## Slide 29: Direct-mapped cache behavior, cont’d.
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
After 101 access:
  block tag data
  00 1 1000
  01 1 0001
  10 0 0000
  11 0 0110
After 111 access:
  block tag data
  00 1 1000
  01 1 0001
  10 0 0000
  11 1 0100

## Slide 30: 2-way set-associative cache behavior
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Final state of cache (twice as big as direct-mapped):
  set blk 0 tag blk 0 data blk 1 tag blk 1 data
  00 1 1000 - -
  01 0 1111 1 0001
  10 0 0000 - -
  11 0 0110 1 0100

## Slide 31: 2-way set-associative cache behavior
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Final state of cache (same size as direct-mapped):
  set blk 0 tag blk 0 data blk 1 tag blk 1 data
  0 01 0000 10 1000
  1 10 0111 11 0100

## Slide 32: Example caches
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
StrongARM:
  16 Kbyte, 32-way, 32-byte block instruction cache.
  16 Kbyte, 32-way, 32-byte block data cache (write-back).
SHARC:
  32-instruction, 2-way instruction cache.

## Slide 33: Memory management tasks
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Allows programs to move in physical memory during execution.
Allows virtual memory:
  memory images kept in secondary storage;
  images returned to main memory on demand during execution.
Page fault: request for location not resident in memory.

## Slide 34: Address translation
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Requires some sort of register/table to allow arbitrary mappings of logical to physical addresses.
Two basic schemes:
  segmented;
  paged.
Segmentation and paging can be combined (x86).

## Slide 35: Segments and pages
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
memory
segment 1
segment 2
page 1
page 2

## Slide 36: Segment address translation
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
segment base address
logical address
range
check
physical address
+
range
error
segment lower bound
segment upper bound

## Slide 37: Page address translation
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
page
offset
page
offset
page i base
concatenate

## Slide 38: Page table organizations
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
flat
tree
page descriptor
page
descriptor

## Slide 39: Caching address translations
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Large translation tables require main memory access.
TLB: cache for address translation.
  Typically small.

## Slide 40: ARM memory management
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Memory region types:
  section: 1 Mbyte block;
  large page: 64 kbytes;
  small page: 4 kbytes.
An address is marked as section-mapped or page-mapped.
Two-level translation scheme.

## Slide 41: ARM address translation
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
offset
1st index
2nd index
physical address
Translation table
base register
1st level table
descriptor
2nd level table
descriptor
concatenate
concatenate

## Slide 42
Overheads for Computers as
Components 2nd ed.
© 2008 Wayne Wolf
Pipelining
Several instructions are executed simultaneously at different stages of completion.
Various conditions can cause pipeline bubbles that reduce utilization:
  branches;
  memory system delays;
  etc.

## Slide 43: Performance measures
Latency: time it takes for an instruction to get through the pipeline.
Throughput: number of instructions executed per time period.
Pipelining increases throughput without reducing latency.

## Slide 44: ARM pipeline execution
add r0,r1,#5
sub r2,r3,r6
cmp r2,#3
fetch
time
decode
fetch
execute
decode
fetch
execute
decode
execute
1
2
3

## Slide 45: Pipeline stalls
If every step cannot be completed in the same amount of time, pipeline stalls.
Bubbles introduced by stall increase latency, reduce throughput.

## Slide 46: ARM multi-cycle LDMIA instruction
fetch
decode
ex ld r2
ldmia
r0,{r2,r3}
sub
r2,r3,r6
cmp
r2,#3
ex ld r3
fetch
time
decode
ex sub
fetch
decode
ex cmp

## Slide 47: Control stalls
Branches often introduce stalls (branch penalty).
  Stall time may depend on whether branch is taken.
May have to squash instructions that already started executing.
Don’t know what to fetch until condition is evaluated.

## Slide 48: Memory system performance
Caches introduce indeterminacy in execution time.
  Depends on order of execution.
Cache miss penalty: added time due to a cache miss.

## Slide 49: Types of cache misses
Compulsory miss: location has not been referenced before.
Conflict miss: two locations are fighting for the same block.
Capacity miss: working set is too large.

## Slide 50: CPU power consumption
Most modern CPUs are designed with power consumption in mind to some degree.
Power vs. energy:
  heat depends on power consumption;
  battery life depends on energy consumption.

## Slide 51: CMOS power consumption
Voltage drops: power consumption proportional to V2.
Toggling: more activity means more power.
Leakage: basic circuit characteristics; can be eliminated by disconnecting power.

## Slide 52: CPU power-saving strategies
Reduce power supply voltage.
Run at lower clock frequency.
Disable function units with control signals when not in use.
Disconnect parts from power supply when not in use.

## Slide 53: data-compressor behaviors
encode: Takes one-byte input, generates packed encoded symbols and a Boolean indicating whether the buffer is full.
new-symbol-table: installs new symbol table in object, throws away old table.
flush: returns current state of buffer, including number of valid bits in buffer.